Description:
This device is a corrosion proof alternative to the typical ring terminals on a stud
approach often found in heavy vehicle and marine applications. The 300 Amp stud
is connected to a fully encapsulated solid copper bar tied in parallel to all connector
terminals. The industry standard Deutsch connector provides a robust time tested
mass termination point.

This device has been successful in mobile applications such as fire fighting apparatus,
construction equipment and marine applications

Available in :
- ABB-GC1625B - coming in BLACK
- ABB-GC1625R - coming in RED

Features:
- Current Rating: 25 A
- Housing Material: Polyurethane
- Ingress Protection: IP67
- Operating temperature: -40 to +85°C

Product Stage: Mass production