Part number :

P/N structure example: AJSC-J1A1-X-001 BH
A	JS	C	-	J	1	A1	-	001	-	X	-	BH / SH / GH
Grade	Unit	Type		Protocol	Axes	CPU type		Model		Modifications		Handle Type
A - Automotive	Joystick	C - CAN		J - J1939	1 Axis	-		-				BH - Ball
I - Industrial		CE - CAN + Com Ext		O - CAN Open		-		-				SH - Steak
					-		-				GH - Grip

Connections:

Cable A - Power & CAN:
Availability	Always
Length	6" (150 mm)
Connector	DT04-4P
Pinout	Pin 1: Battery + (Power) / Pin 2: Battery - (Ground) / Pin 3: CAN High / Pin 4: CAN Low

Cable B - Communication Extension:
Availability	Optional (only upon customer request)
Length	4" (100 mm)
Connector	DT06-4S
Pinout	Pin 1: Common Power / Pin 2: Reserved / Pin 3: Platform Down Signal (active High) / Pin 4: Platform Up Signal (active High)