	MECHANICAL
	AJSC-J1A1-001 GH	AJSC-J1A1-001 SH	AJSC-J1A1-001 BH

Length	4" (102 mm)
Height	8.5" (215 mm)	8.5" (215 mm)	5.5" (140 mm)
Depth	2" (52 mm)
Material	Diecast Aluminum Alloy	Diecast Aluminum Alloy	Diecast Aluminum Alloy
Weight	435 g	420 g	400 g
	ENVIRONMENTAL
Operating Temperature	-40°C to 85°C
Storage Temperature	-50°C to 85°C
Vibration	Level ±3g, 10Hz to 200Hz (random) @ 3.6g(rms)
Shock	20g, 6mS, half sine profile
Life Cycle	10 million operations
EMC Immunity Level	100V/m, 30MHz to 1GHz, 1KHz 80% sine wave modulation, EN50082-2
EMC Emissions Level	Complies with EN50081-2 (1993), 150kHz to 30MHz, level B
	ELECTRICAL
Voltage (Supply)	6.5-38 VDC
Current (Supply)	< 25mA
Over Voltage	Up to 50 VDC for 2 sec
Threshold voltage	3.2 V+/-5%
Reverse Polarity Protection	YES
Input Resistance	NO
	GENERAL
Supported Technology	MOTOPLEX
Protocols	CAN J1939
Baud Rate	250 kbit/s