Description

A single-axis, joystick controller is designed for mobile applications and features robust packing, wide temperature and voltage tolerance as well as strong EMI and ESD immunity.
The AJSC-J1XX joystick utilizes contact-less, position-sensor technology combined with a rugged, low-profile design. It features an ARM micro-controller running the 621 co-operative multi-tasking kernel to provide a light high performance solution.
Protocols include Generic CAN, J1939 or CAN Open protocol.

Features

- Safety Critical Spec available
- Protocols include Generic CAN, J1939 or CAN Open protocol.
- Contact-less - Hall-effect technology
- Single-axis control with mechanical neutral safety switch
- Choice of handles and grips
- Extended IO (Optional)
- Operating temperature -40 to +85°C

Product Stage: Mass production