	MECHANICAL

Length	9.0" (228 mm)
Height	3.5 (88 mm)
Depth	3.7" (94 mm)
Material	Aluminum Alloy
Finishing	Powder Coated
Weight	890 g
	ENVIRONMENTAL
Operating Temperature	-40°C to 85°C
Storage Temperature	-50°C to 85°C
Vibration	Level ±3g, 10Hz to 200Hz (random) @ 3.6g(rms)
Shock	20g, 6mS, half sine profile
Life Cycle	100 000 hours
EMC Immunity Level	100V/m, 30MHz to 1GHz, 1KHz 80% sine wave modulation, EN50082-2
EMC Emissions Level	Complies with EN50081-2 (1993), 150kHz to 30MHz, level B
	ELECTRICAL
Voltage (Supply)	6.5-38 VDC
Current (Supply)	< 25mA
Over Voltage	Up to 50 VDC for 2 sec
Threshold voltage	3.2 V+/-5%
Reverse Polarity Protection	YES
Input Resistance	20 KΩ
	GENERAL
Supported Technology	MOTOPLEX
Protocols	CAN J1939
Baud Rate	250 kbit/s