Description
The device provides 16 common pins on all pins 3 and 4 of all connectors -
typically used as the return circuit for the power supply.

The master connector is intended to be connected to two power supplies on Pin 1
and Pin 2. Pin 1 and Pin 2 of each slave features a current limited output.

The device is designed for mobile applications and features robust Deutsch
Connectors and a fully potted package, wide temperature and voltage tolerance as well
as strong EMI and ESD immunity.

Features
- Operating temperature -40 to +100°C
- Protocols include Generic CAN, J1939.
- Rugged, diecast aluminum alloy enclosure.
- Military grade conformally coating plus SilGuard potting.
- Field proven Deutsch DT Series connectors.

Product Stage: Prototype