Part number structure: AZEI-002-SSI1
A	ZEI	-	2	-	211001	-	SSI2	-	PA
Automotive	ZETTLEX Encoder Interface		Model Number / 001 / 002 / .....		Supported Communication Format		Interface identifier: / SSI1 / SSI2		Enclosure / Type / PA / PB / PC

Example Application:
Zettlex IncOder / Netzer SSI Encoder interface
Protected power supply output for encoder.
Set Zero
Reset Factory Zero

Firetruck Ladder Control interface:
Auxiliary Port used to power cradle align signal.

Data Transmission Options:
- Protocol J1939/CANOpen
- CAN Transmission Speed
- CAN Packet Speed - including dynamic speed (faster packet rate while moving)

Data Sampling Options:

- 10 to 22 bits per revolution
- SPI Format (Serial Peripheral Interface)
- SSI (Synchronous Serial Interface) SSI1 - SSI9 , SSI2&7(Parity) and SSI6(CRC)  - Recommended.
- ASI (ASync)

Data Processing Options:
- Encoder Data: Most Recent, Mean, Mode, Median
- Number of sub-samples per sample
- Sample Period
- Transmission Threshold

Example #1 :
CAN Packet Rate: 100mS Fixed
Data Processing: Most Recent
Result: Every 100mS the device will sample the encoder and immediately transmit the data on the CAN network.

Example #2 :
CAN Packet Rate: 25mS/3000mS Dynamic
Threshold: 10
Data Processing: Most Recent
Result: Every 25mS the device will sample the data.  If the data has changed by 10 or more counts, the data will be transmitted on the Network.  If the data does not change substantially for 3000mS, a heartbeat transmission will occur to indicate that the device is still healthy and available on the Network

Example #3:
CAN Packet Rate: 100mS Fixed
Data Processing: Mode
Samples: 5
Sample Period: 5mS
Result: Every 100mS the device will sample the encoder 5 times at 5mS intervals. The most frequently occurring data will be then be immediately transmitted on the Network. If no data pattern re-occurs - then the median will be transmitted.

Example #4:
CAN Packet Rate: 100mS Fixed
Data Processing: Median
Samples: 5
Sample Period: 5mS
Result: Every 100mS the device will sample the encoder 5 times at 5mS intervals. The centermost data pattern will be then be immediately transmitted on the Network.

Example #5:
CAN Packet Rate: 100mS Fixed
Data Processing: Mean
Samples: 5
Sample Period: 5mS
Result: Every 100mS the device will sample the encoder 5 times at 5mS intervals. The average of all data patterns will be then be immediately transmitted on the Network.