	MECHANICAL
	AZEI-002-XXXXXX-XXX-PA	AZEI-002-XXXXXX-XXX-PB	AZEI-002-XXXXXX-XXX-PC

Length	4.35" (110 mm)	5.5" (140 mm)	4.5" (115 mm)
Height	2.2" (56 mm)	2.2" (56 mm)	1.7" (42 mm)
Depth	3.75" (95 mm)	3.2" (82 mm)	3.5" (90 mm)
Material	Die-cast Aluminum Alloy	Die-cast Aluminum Alloy	Machined Aluminum
Finishing	Vibra Finished	Vibra Finished	Anodized
Weight	360 g	355 g	400 g
	ENVIRONMENTAL
Operating Temperature	-40°C to 85°C
Storage Temperature	-50°C to 85°C
Vibration	Level ±3g, 10Hz to 200Hz (random) @ 3.6g(rms)
Shock	20g, 6mS, half sine profile
Life Cycle	100 000 hours
EMC Immunity Level	100V/m, 30MHz to 1GHz, 1KHz 80% sine wave modulation, EN50082-2
EMC Emissions Level	Complies with EN50081-2 (1993), 150kHz to 30MHz, level B
	ELECTRICAL
Voltage (Supply)	6.5-38 VDC
Current (Supply)	< 25mA
Over Voltage	Up to 50 VDC for 2 sec
Threshold voltage	3.2 V+/-5%
Reverse Polarity Protection	YES
Input Resistance	20 KΩ
	GENERAL
Supported Technology	MOTOPLEX
Protocols	CAN J1939
Baud Rate	250 Kbit/s