Technical Specifications: All voltages are RMS unless otherwise specified. All specifications typical at nominal input voltage and 25 degrees C unless otherwise specified.

Operating Voltage: 18VAC 24VAC 48VAC 120VAC 240VAC
LINE Side Max. Input Voltage	20VAC	30VAC	60VAC	130VAC	270VAC
PROTECTED Side Voltage Level Suppression Begins: / Stage Two Stage Three	30V / 35V	42V / 50V	90V / 110V	175V / 195V	390V / 440V
Max. Clamp Volts for Maximum Transients on Line: / Stage Two Stage Three	65V / 77V	93V / 110V	165V / 200V	340V / 360V	710V / 775V
Surge Current: / 8/20Sec Pulse L to N / L to E N to E	9000A / 4000A / 4000A	9000A / 4000A / 4000A	30500A / 13000A / 13000A	36500A / 16000A / 16000A	28500A / 16000A / 8000A
2mSec Pulse L to N L to E N to E	94J / 44J / 44J	139J / 66J / 66J	177J / 80J / 80J	346J / 156J / 156J	590J / 346J / 173J
Response Time	<5 nSec	<5 nSec	<5 nSec	<5 nSec	<5 nSec
Resistance to Earth: Max. Over-Voltage Operating Voltage	0.01 Ohm / >1 MOhm	0.01 Ohm / >1 MOhm	0.01 Ohm / >1 MOhm	0.01 Ohm / >1 MOhm	0.01 Ohm / >1 MOhm

Packaging / Dimensions:	WEG 6 terminal modular housing, #12 to #22 AWG terminals
# Size: 60.6 mm x 90.5 mm x 22.5 mm (2.39" x 3.56" x 0.89")
(W x H x D excluding DIN Rail)
Operating Conditions:	-40 to +85oC (-40 to 185F), 0 to 93% Relative Humidity

Ordering Part Number:	With Indicator
# 18VAC 10A ... WB.700.143
24VAC 10A ... WB.700.144
48VAC 10A ... WB.700.145
120VAC 10A ... WB.700.120
240VAC 10A ... WB.700.121

Variations are available by special order.

Specifications are subject to change without notic